## Slide 1: GIS Basics for Beginners
Watson Harding
GIS Specialist
Kentucky 911 Services Board

## Slide 2: Outline
Section 1: GIS Basics
  a. What is GIS?
  b. GIS and Next Generation 9-1-1
  c. GIS Software Options
Section 2: Tips and Tricks
Section 3: Questions

## Slide 3: What is GIS?
GIS stands for Geographic Information Systems
  A computer system that analyzes and displays geographically referenced data
    Ex. A Fire Hydrant layer contains both points representing the location of hydrants and the attributes of every individual hydrant such as flow capacity, last inspection
Commonly points, lines, and polygons
Geometry=Spatial properties, Attributes=Table data

## Slide 5: GIS is Foundational to Next Generation 9-1-1
At its most basic, the goal is to connect the caller with the correct PSAP as quickly as possible while minimizing complications (transfers, etc.)
This works through the relationship of the cellular device and PSAP Boundaries (Geospatial Routing)
  The phone broadcasts its location, a point, and compares it to PSAP Boundaries, polygons. The call is routed to the PSAP polygon in which the caller’s point is located.

## Slide 6: It’s a little more complicated than that…

## Slide 7: GIS and NG911
NG911 is coming
  KY911SB has been allocated funding and is in the RFP process
Need statewide layers, without gaps and overlaps
  Created by aggregation of PSAPs’ GIS data submissions
KY911SB contracted with GeoComm to QC and aggregate submissions
  Project Page
  GeoComm KY Team Email
  NENA GIS Data Model

## Slide 8: Upload Process
PSAPs submit their package with all required layers by uploading to GeoComm’s browser-based GIS Data Hub
  Can ingest zipped Shapefiles and Geodatabases, more later
Fields mapped to NENA GIS Data Model
The submission is ran through attribute and geometry checks
If submission is free of critical errors, it is aggregated into statewide layers. Otherwise a Fallout Report generated.

## Slide 9: Requirements
Every PSAP must upload their GIS Data once per quarter
Notify Board and GeoComm of personnel changes
Help always available
  Watson.Harding@ky.gov
  GCTeamKY911@geo-comm.com

## Slide 10: NG911 GIS Data Layers
Provisioning Boundary: the polygon layer that assigns responsibility for the data within that polygon
  If you need to create, same geometry as PSAP Boundary with small number of attributes
PSAP Boundary: the polygon layer that the caller location is hitting against
  Answers “where should the call go?”
  Often initially based on existing boundaries like county
  Real life is more complicated and should consider access etc.
  Need agreement with neighboring PSAPs, contact us for contacts and guidance

## Slide 11
PSAP B
PSAP A
Overlap

## Slide 12: The PSAP Boundary is All
All GIS Data should be within, or coincident with PSAP Boundary
The PSAP Boundary should never be ‘empty’

## Slide 13: NG911 GIS Data Layers
Responder (Emergency) Services Boundaries: polygon layers for Law, Fire, and EMS
  Attaches responder information to the incoming call
Road Centerlines: polyline layer used, if needed, to locate caller based on road address ranges
Site and Structure Address Points: point layer of, at minimum, addressed structures
  Attaches nearest address, within tolerance, to the incoming call
Simple explainer

## Slide 14: Should I collect it?
The minimum is addressed structures
  Don’t forget notable subunits
    Apartments
Multiple structure points
  Can share same address number
  Differentiated by fields like Building
Collect what can be maintained
  And what is most useful

## Slide 15: SSAP Challenges
There aren’t limits to potential granularity
Current data is better than obsolete data
Elevation (Z-axis) harder to accurately capture than x,y
  Improvements needed from carriers
  Affects tall multistory buildings
Need the PSAP community to share their experiences and best practices

## Slide 16: Kentucky’s Current Progress

## Slide 17: Are we done yet?
GIS Data needs to be maintained and kept current
GIS Data Hub has limits
  Great for attribute checks
  Geometry checks will indicate some issues
  It won’t tell you if a road centerline isn’t properly aligned or house demolished
Almost every PSAP has contributed their ‘piece’ of the puzzle
  Now we must put it together and keep it current

## Slide 18: Internal or External Workforce
Who can you hire to maintain your data?
  Datamark, GeoComm, CDP-MapSync, and others
  Area Development Districts
Maintaining your data internally
  Costs: software, salary, and time
  Collaborate with other parts of local government

## Slide 19: GIS Software Options
ArcGIS: umbrella term for software published by ESRI, the main originator and developer of GIS software
QGIS: a free and open-source GIS software product like other open-source products (OpenOffice, Firefox, Linux, etc.)
Third Party Editors: software products commonly built on ESRI software with simplified functionality
  Ex. GeoConex GIS Map

## Slide 20: ArcGIS 10.x
Last version 10.8.2
Support set to end
Have a plan to transition

## Slide 21: ArcGIS Pro 3.3
ESRI business trends are towards greater integration with ArcGIS Online (AGOL), subscription model, web-based analysis
Be aware of license levels
  Creator (Basic) lacks functionality needed
  Professional (Standard) sufficient, $2,200/yr
Most add-ons, extensions, and extra credits are unnecessary
Licensing managed in AGOL account

## Slide 22: QGIS
Open-Source (Free)
Comparable functionality to ArcGIS
Smaller userbase, different learning curve

## Slide 23: Third Party Mapping Software
Provide a simplified map viewer and editor
Can lack functionality for user to make necessary edits
Can complicate workflows

## Slide 24: Training
Free resources out there, may require digging
ESRI and QGIS have free tutorials
My advice: get your toes wet

## Slide 25: Tips and Tricks
Shapefiles vs. Geodatabases
Demos
  Understanding where your data “lives”
  Selections
  Field Calculations

## Slide 26: Shapefiles vs. Geodatabases
Two most common file storage methods
Shapefiles
  Still commonly used
  Be aware of subfiles
  Become unstable when large

## Slide 27: Shapefiles vs. Geodatabases
Geodatabases
  Technically ESRI proprietary format, conversion to and from in QGIS
  Greater functionality
    Domains
    Topology
  Can export to shapefile if needed

## Slide 28: Uploading
With shapefiles, verify that all layers and constituent files in the same folder
  Send to Zip
With geodatabase, verify all needed layers within
  Send to Zip

## Slide 29: Questions?
Watson.Harding@ky.gov